CPS Solar panel 210wp/PLOY 156*156

| TYPE | CRM210S/POLY |
| --- | --- |
| MONO or POLY | POLY |
| Maximum power (Wp) | 210wp |
| Maximum power voltage (V) | 29.1 |
| Maximum power current (A) | 7.22 |
| Open circuit voltage (V) | 36.1 |
| Short circuit current (A) | 8.02 |
| Number of cells (Pcs) | 60 |
| Size of module (mm) | 1640*990*40( 156*156mm cell) |
| Size of glass(mm) | 1634*984*3.2 |
| Maximum system voltage (V) | 1000 |
| Temperature coefficients of Isc (%) | 0.065+/-0.015%/℃ |
| Temperature coefficients of Voc (%) | -（2.23+/-0.1）mv/ ℃ |
| Temperature coefficients of Pm (%) | -（0.5+-0.05）/ ℃ |
| Temperature coefficients of Im (%) | +0.1/ ℃ |
| Temperature coefficients of Vm (%) | -0.38/ ℃ |
| Temperature Range | -40℃～+85℃ |
| Tolerance Wattage (e.g. +/-5%) | +/-5% |
| Surface Maximum Load Capacity | 60m/s(200kg/sq.m) |
| Allowable Hail Load | 227g steel ball fall down from height |
| Cell Efficiency (%) | ＞14.25% |
| Output tolerance (%) | +/-5% |
| Frame (Material, Corners, etc.) | Aluminum |
| Standard Test Conditions | AM1.5 100mW/cm2 25’C |
| Warranty | 2 years product warranty and 25 years 80% of power |
| FF (%) | 78% |
| Packing | 2PCS/CTN |