ISKANDER MARINE SARL

40' X 8' 6" Refrigerated ISO Cargo Container

CARRIER  1992 et 1993

Etat  général d’occasion  = révise et répare  perfectement.

— STANDARD FEATURES —

Isolation /Insulation : mousse de polyurethane/ polyurethane foam

Aluminum, steel or sides

Double full opening swing doors on

one end

Aluminum T-grade floors

Most refrigerated machinery features

electrical supply as follows: 208/230,

380/460 Volts AC,

3 phase, 50 or 60 cycle

Isolation/Insulation: mousse de polyurethane foam

Temperature range from -20° F to 70° F

40' Refrigerated

40’ Reefer                          Length                           Height                            Width                  Door Opening

Exterior   Interior        Exterior    Interior       Exterior      Interior          Height        Width

Feet/Inches           40' 0"    38' 0 3/4"           8' 6"      7' 3 5/8"      8' 0"          7' 5 5/8"            7' 6 1/2"     7' 5 5/8"

Metric                12,192        11,602            2,591          2,226       2,438             2,276                   2,199         2,276

Passage de portes (en m)  2,199

40' Refrigerated              Tare Weight              Payload             Gross Weight        Cubic Capacity

Lbs.                                       10,000                     60,000                   67,200                   2,076 Cu. Ft.

Kg.                                        4,600                       28,000                   30,480                    58.8 Cu. M.

| Tare weight | 4,650 Kg | 10,253 lbs |
| --- | --- | --- |
| Internal cube | 58.8 m³ | 2,076 ft³ |
| Internal LxWxH | 11,583 x 2,286 x 2,994mm | 456 x 90 x 118in |
| MGW | 32,800 Kg | 72,324 lbs |
| Payload | 28,150 Kg | 62,071 lbs |
| Stacking height | 7 high |  |
| Top & Bottom rails | Corten |  |
| End Frames | Corten |  |
| Outer panels | MGSS welded |  |
| Underfloor | Corten crossbearers |  |
| Inner roof | Aluminium |  |
| Tee floor height | 63.5mm |  |
| Door outer | MGSS |  |
| Lock rods | 4 |  |
| Goose neck tunnel | Fitted |  |
| Fork lift pockets | No |  |
| Manufacturer | Hyundai |  |
| Machine manufacturer | Carrier |  |
| Refrigerant | R134a |  |
| Model | NNT40-489/511 |  |
| Voltage | 415/3ph - 220V Option |  |
| Chart recorder | Option |  |
| Data memory | Yes |  |

ALL NEW CONTAINERS ARE

MANUFACTURED TO THE LATEST ISO

STANDARDS FOR 9 HIGH STACKING

- All dimensions are average. Exact specifications for each model are available.

Isolation/Insulation: mousse /polyurethane foam Isolation/Insulation: mousse de foam

Isolation/Insulation: mousse foam